## Slide 1: Events Detection

## Slide 2: Log Book – Sensors
25 sensors:

## Slide 3: Log Book - Events
Currently, we ignore columns: A, B, E, F. How can we use them?
Tools Classes: {‘h’, ‘j’, ‘n’} and quite: {‘x’}
Distractor Classes: {‘v’, ‘d’} and quite: {‘x’}
We assume quite times if not mention otherwise. (e.g. 12:35 – 12:45)
Overall, 12 different combinations can be composed. E.g. or etc.
What is accuracy of start and end time??

## Slide 4: Input Data

## Slide 5: Quite?

## Slide 6: Classification approach – Features selection
The raw data is from a huge dimension
  Hours of recording (sampling rate = )
  25 channels
We convert each distinct 5 seconds from the data into a single feature vector, namely: .
5 Sec
All 25 channels
Features Selection

## Slide 7: Approach for features selection
Our approach is based on Geometry analysis & learning.
For now, we test only spatial features:
  For each time leg we estimate the covariance matrix, namely
The covariance matrices are all positive definite. Thus, they are lay on the manifold , which embedded in the space of symmetric matrices.
On this manifold we use a Riemannian metric instead of the naïve Euclidean metric.

## Slide 8
12:00 – 13:30
4 events
Class 0 - No event
Class 1 - Event
Overall 93.6%
We assume most error occur due to coarse labeling.
Preliminary Results - Event Detection

## Slide 9: Preliminary Results
Removing quite times. (so either distractor or tool is in the log –book).
11 Classes.
2,396 samples.
Using Ensemble Subspace Knn: 94.8% accuracy.
No Tool
Tool ‘h’
Tool ‘j’
Tool ‘n’

## Slide 10: Comparison to Euclidean Metric
Removing quite times. (so either distractor or tool is in the log –book).
11 Classes.
2,396 samples.
Using Ensemble Subspace Knn: 84.8% accuracy.
No Tool
Tool ‘h’
Tool ‘j’
Tool ‘n’

## Slide 11: Summary
This is an early stage solution for managing expectations.
Simple approach: detection and classification under supervised setting.
Main result: the discrimination capability of the features and the metric.
what should be the framework? supervised / unsupervised, available sets of all possible tools and distractors.
Next step, incorporate time using kernels and new definitions of Riemannian metrics for joint time and space geometry analysis.
Discussion